# GSR Response
The GSR Response detection is a part of the Biosig plugin. It consists of 3 classes: The most important one is the GSRResponseDetection class. Here a functions to detect responses in a raw signal. The GSRResponseEventSender class uses this detection functions to send events which contain the response’s features. The features are: minimum, maximum, amplitude, duration, time, energy and power. The GSRResponseEventListener converts the event features to a number of responses, amplitude, rising time, power and energy signal. It is possible to use a window and a statistical function to aggregate the events inside the window. The statistical functions are: Sum, mean, variance, standard deviation and could be applied to the features.

# How the GSR Response detection works.
The Algorithm is based on finding local minima and maxima. As it gets one sample after another passed over it first looks for a minimum. The current minimum is saved with its value and time. If the next sample is smaller, the minimum gets overridden. If the difference between the values of the current minimum and the next sample(s) values gets greater than the threshold “minAmplitude” and the difference in time of the current minimum and the next sample(s) is greater than the threshold “minRisingTime” then the algorithm starts looking for a maximum.
First the current value is saved as a maximum. Afterwards every value that is greater than the current maximum overrides the current maximum. As the minimum value, the maximum is saved with value and time. Once the maximum is found and the next incoming values start to decrease, the difference in value between the saved maximum and the next samples must be greater than the threshold “minAllowedRegression” for a complete response to be detected.